## Slide 1: Computational Photography
Xiaowei Deng
Course Advisor: Dr. Shirani
Dec. 10, 2013
Notes: Good morning, everyone.
My name is Xiaowei Deng. Now I’m going to try my best to share with you what I learnt in these days for the charter 10: about computational photography.
Actually, Computational photography is an emerging field that aims to overcome the limitations of conventional digital imaging and display devices by using computational techniques and novel coded optical devices and sensors to perform more efficient and accurate measurement as well as produce more compelling and meaningful visualizations of the world around us.
It is a convergence of many areas, such as computer vision, computer graphics, image processing, photography, and so on.

## Slide 2: Outline
Photometric calibration
High dynamic range imaging
Image matting and compositing
Super-resolution and blur removal
Texture analysis and synthesis
Notes: In today’s Lecture, I will cover topics of Photometric calibration, High dynamic range imaging, Super-resolution and blur removal, image matting and compositing, Texture analysis and synthesis.

## Slide 3: Outline
Photometric calibration
High dynamic range imaging
Image matting and compositing
Super-resolution and blur removal
Texture analysis and synthesis
Notes: Let’s first start with photometric calibration.

## Slide 4: Image sensing pipeline
Photometric calibration
Notes: Please let me show you a image sensing pipeline first, which give the procedure of how digital image is generated.
Basically, the scene radiance will go through camera body into the sensor chip, and the camera will also do a simple image processing on the raw image data.
And what we need to characterize is the functions that map incoming irradiance and the output pixel values
What else we care for including the amounts of noise present in each image.

## Slide 5: Calibration
Radiometric response function
Noise level estimation
Photometric calibration
Notes: basically, I will focus on two components, the methods for radiometric response function, Noise level estimation

## Slide 6: Radiometric response function
Affect Factors:
1. Aperture and shutter speed
2. A/D converter (controlled by ISO, linear)
3. Demosaicing
Photometric calibration
Notes: This is how A typical radiometric response function looks like :
The x axis shows the exposure values, which usually in log 2 ratios, the Y axis shows the pixel values Z, most times, like in RGB channel, ranges from 0 – 255.
There are many factors that will affect the function. Basically, there are 3 things here:….
As you can see, it is very hard to model the camera response function, that is the mapping between incoming irradiance and digital RGB values.
So next, I’m going to show you some practical approaches to calibrate the camera by measuring the correspondences between incoming light and final values.

## Slide 7: Why calibrate
Using Samsung Phone
Photometric calibration
Using iPhone
Notes: By the way, I want to give you simple intuition for why we should do calibration.
Here I took two pictures in the same place using two different devices, we can see that there is a color difference here: the picture on the right is kind of more red.
And if we focus on here: we can see that we on the left, we cannot see the edge of the paper. This is also a specific name for this issue called High dynamic range imaging. Which I will talk to you later.

## Slide 8: Approaches to measure response function
Integrating sphere
Photometric calibration
Notes: The most accurate, but also most expensive way in to use an integrating sphere.
A typical sphere is a large one, the inside painted with white matte paint.
This device can make the irradiance constant everywhere inside the sphere, and we can accurately control the light exposure.
There is a small opening at the side can allows for a camera combination to be mounted as well.
In this way , we can establish the response between incoming radiance and measured pixel values.

## Slide 9: Approaches to measure response function
Calibration chart
Photometric calibration
http://www.adorama.com/alc/0013301/article/Using-the-ColorChecker-Passport-Adorama-TV
Notes: There is another way, which is more practical, to measure response, is to use calibration chart.
Actually, when using this method, you have to carry the colorchecker chart to shoot in the same lighting as your images;
And Then you can use a photo processing software, like photoshop, to deal with color correction.
What you’re going to notice is that this approach must ensure uniform lighting. So do not place the chart under shadows.
Here is the website, gives a video tutorial on how to use the chart.
So if you are a Photography lovers, you can use this way to generate a more realistic, higher quality photographs .

## Slide 10: Approaches to measure response function
Multiple images’ algorithms
Photometric calibration
Notes: Actually, there is another way to use multiple images to calculate the response function, which is widely used in HDR image processing.
It is like you have more than one images, you can use these information to reconstruct the response function.
I think I’ll cove the detail algorithms later.

## Slide 11: Noise level estimation
Photometric calibration
Notes: another important thing, I’m going to tell you, is noise level estimation,
When you shoot a picture, especially there is no enough light, you camera will generate noises everywhere.
The question is how to xiaochudetect these noise and Eliminate the noise here.

## Slide 12: Approaches to measure noise
Integrating sphere
Calibration chart
Taking repeated exposures and computing the variance(Healey and Kondepudy 1994)
Assuming pixel values should all be the same within some region.(Liu, Szeliski, Kang et al.2008)
Photometric calibration

## Slide 13: Approaches to measure noise
Integrating sphere
Calibration chart
Taking repeated exposures and computing the variance(Healey and Kondepudy 1994)
Assuming pixel values should all be the same within some region.(Liu, Szeliski, Kang et al.2008)
Photometric calibration

## Slide 14: Noise Estimation from a Single Image(Liu,2008)
Where is the observation and
Photometric calibration
Notes: In his paper, He defines the noise level function(NLF) as the variation of the standard deviation of noise with respect to image intensity.
Basically, or Essentially, this is a function of how standard deviation changes with respect to the mean value.
And Our goal is to infer this function.

## Slide 15: Step 1. Segmentation
Step 1.
Segment the image in to regions and fit a constant or linear function inside each region
Photometric calibration

## Slide 16: Step 2. Measure deviation
Patch
=
+
Signal
Residual
For each RGB channel:
Brightness mean I
Standard deviation s
Red
Green
Blue
0 0.5 1
0.2
0.1
0
I
s
0 0.5 1
0.2
0.1
0
I
s
0 0.5 1
0.2
0.1
0
I
s
Brightness
Standard deviation
Affine model
Photometric calibration
Notes: The idea of Liu’s paper in 2008 is like this.
He assume that there are regions of constant or slowly varying intensity to photos .

## Slide 17: Step 2. Measure deviation
Patch
=
+
Signal
Residual
Red
Green
Blue
0 0.5 1
0.2
0.1
0
I
s
0 0.5 1
0.2
0.1
0
I
s
0 0.5 1
0.2
0.1
0
I
s
Brightness
Standard deviation
Photometric calibration

## Slide 18: Step 2. Measure deviation
Patch
=
+
Signal
Residual
Red
Green
Blue
0 0.5 1
0.2
0.1
0
I
s
0 0.5 1
0.2
0.1
0
I
s
0 0.5 1
0.2
0.1
0
I
s
Brightness
Standard deviation
Photometric calibration

## Slide 19: Step 3. Fit a lower envelope
Assume brightness mean I is accurate estimate
Standard deviation s is an over-estimate: (may contain signal)
The lower envelope is the upper bound of NLF
s
s
s
I
I
I
Brightness
Residual std. dev.
Photometric calibration

## Slide 20: Noise Estimation from a Single Image(Liu,2008)
Results
Using standard bilateral filter
Using adaptive bilateral filter(para by deviation of the noise)
Photometric calibration

## Slide 21: Noise Estimation from a Single Image(Liu,2008)
CCD camera noise model:
Noise level function:
Photometric calibration
Notes: Step 2:The Prior of NLFs
before we infer the NLF, we can get a prior of NLF.
Actually, because we know that CCD camera noise model is like this,
dairu our NLF , we can get the new noise level function:

## Slide 22: Noise Estimation from a Single Image(Liu,2008)
Using numerical simulation, the noise function, for each of red, green and blue channels, we can get:
Noise level function:
Photometric calibration
Notes: So our goal is try to infer the actually coefficients on the eigenvectors:
Beta1 2 3 …

## Slide 23: The Prior of NLFs
Photometric calibration

## Slide 24: Likelihood Function
The estimated standard deviation should be probabilistically bigger than and close to the true value
Bayesian MAP inference
I
Photometric calibration

## Slide 25: Noise Estimation from a Single Image(Liu,2008)
Likelihood model
Photometric calibration
Notes: Step 3: Likelihood Model

## Slide 26: Noise Estimation from a Single Image(Liu,2008)
Bayesian MAP Inference
Photometric calibration

## Slide 27: Outline
Photometric calibration
High dynamic range imaging
Super-resolution and blur removal
Image matting and compositing
Texture analysis and synthesis
Notes: The next part I’m going to show you is the High dynamic range imaging.

## Slide 28: High Dynamic Range
High dynamic range imaging
Notes: And in my later lecture for high dynamic range imaging, I will show you how to use a algorithm to calculate the function.
The second topic which I want to show you is so called high-dynamic range image processing.
What is high dynamic range actually? In the pic, we can see that some parts are overexposed while some parts are underexposed. We can can not see all the details for the whole picture.
the areas outside the window are overexposed and inside the room are too dark, or we can say that is underexposed.

## Slide 29: The Problem of Dynamic Range
The real world is high dynamic range!
1
1500
25,000
400,000
200,000,000
High dynamic range imaging
Notes: Unfortunally, the problems are very common. The dynamic range ratio for the real word could be as high as like 200 million.

## Slide 30
Today’s Cameras: Limited Dynamic Range
We need about 5-10 million values to store all brightnesses around us.
But, typical 8-bit cameras provide only 256 values!!
High Exposure Image
Low Exposure Image
10-6
106
10-6
106
Real world
Picture
0 to 255
High dynamic range
Long Exposure
Short Exposure
High dynamic range imaging
Notes: The problem is like,
If you shoot a very bright thing, like the sun in the sky, you have to use a very short exposure time. But if you want to shoot the star or moon at light, you have to use long exposure.
But the realistic scenario has more that 5 million values of brightness, and our camera can only provide 256 values..
Basically, we should have a special non-linear mapping function to regenerate a better view picture.

## Slide 31: AEB mode and HDR Composite
High dynamic range imaging
Notes: Actually, we can take a set of bracketed exposures images by using camera’s automatic exposure bracketing mode.
Obviously, These three pics are using over-exposure, normal exposure, under-exposure.
If we combine them together using some techniques, we can get a relatively better one.

## Slide 32: Recovering HDR
1. Extract the radiance information from the photographs
2. Tone-map it into a single low dynamic range image
High dynamic range imaging
Notes: Basically, we have 2 steps to generate a better composition picture.
To turn a photograph into an HDR image, we first extract the radiance information from the photographs and then tone-map it into a single low dynamic range image.

## Slide 33: Recovering HDR
1. Extract the radiance information from the photographs
2. Tone-map it into a single low dynamic range image
High dynamic range imaging
Notes: Basically, we have 2 steps to generate a better composition picture.
To turn a photograph into an HDR image, we first extract the radiance information from the photographs and then tone-map it into a single low dynamic range image.

## Slide 34: Recover radiance map (Debevec. 1997)
High dynamic range imaging
Given multiple exposure pictures
Goal: estimating the radiometric response function( radiance map )
Notes: For the first step, to estimate the radiance map, I’m going to show you the algorithms proposed by Debevec@1997. It is very simple but affective method.

## Slide 35: Recover radiance map (Debevec. 1997)
The radiance map can be written as:
Where is the radiance at position i.
Define as the exposure.
Known: ,
Unknown: , f
At Position i
=f( )
High dynamic range imaging
Notes: Before we get started with the math, I should show you what’s going on here when we use camera to take pictures with different exposure.
We can see that for a static scenario, if we take different exposure pictures, we can get 3 different values at the same position.
The mapping function between the exposure and image value are function f.
We want to recover the function f and the irradiances Ei that best satisfy the set of equations arising from this equation.
Here we suppose that we know the exposure time t for each picture,

## Slide 36: Recover radiance map (Debevec. 1997)
Note: recovering g only requires recovering finite number of values.( Since the domain of Z is from 0-255)
=f( )
()=( )
can be rewrite as:
() =
, taking the natural logarithm of both sides, we have:
() =
, to simplify notation, let g=f-1
High dynamic range imaging

## Slide 37: Recover radiance map (Debevec. 1997)
Objective function:
High dynamic range imaging
Notes: So apparently, we can come up with this following quadratic objective function:

## Slide 38: Recover radiance map (Debevec. 1997)
Refine objective function:
1. scalar function:
2. anticipating the basic shape of the response function:
High dynamic range imaging
Notes: First, we should have a scalar function here. Because you can see that if we put lnEi as lnEi+constant, and function g plus a constant, the objective function would remain unchanged. So we should introduce the additional constraint function.
Sencondly, because we know the basic shape of the response function: the g(z) will typically have a steep slope near 0 and 255 so we introduce a weighting function here.
This weigting func means that near edge of domain the curve could be very slope.

## Slide 39: Recover radiance map (Debevec. 1997)
Refine objective function:
3. How many samples(pixels) do we need to calculate:
High dynamic range imaging
1.Make sure (# of Ei)*(# of Pictures)>256
2.The pixel locations should be chosen so that they have a reasonably even distribution of pixel values.
Notes: Mathematically, we have to solve for N valudes of Ei in P photographs, and 256 value of pixels. To ensure a sufficient overdetermined system, we need N*P> 256

## Slide 40: Recover radiance map (Debevec. 1997)
Matix representation
High dynamic range imaging
Notes: Actually, if we use matrix representation, it is like this:

## Slide 41: MATLAB CODE
function [g,lE]=gsolve(Z,B,l,w)
n = 256;
A = zeros(size(Z,1)*size(Z,2)+n+1,n+size(Z,1));
b = zeros(size(A,1),1);
k = 1; %% Include the data-fitting equations
for i=1:size(Z,1)
for j=1:size(Z,2)
wij = w(Z(i,j)+1);
A(k,Z(i,j)+1) = wij; A(k,n+i) = -wij; b(k,1) = wij * B(i,j);
k=k+1;
end
end
A(k,129) = 1; %% Fix the curve by setting its middle value to 0
k=k+1;
for i=1:n-2 %% Include the smoothness equations
A(k,i)=l*w(i+1); A(k,i+1)=-2*l*w(i+1); A(k,i+2)=l*w(i+1);
k=k+1;
end
x = A\b; %% Solve the system using SVD
g = x(1:n);
lE = x(n+1:size(x,1));
20 lines !
High dynamic range imaging

## Slide 42: Recover radiance map (Debevec. 1997)
Constructing the HDR Radiance Map
High dynamic range imaging

## Slide 43: Results: Color Film
Kodak Gold ASA 100, PhotoCD
High dynamic range imaging
Notes: 14

## Slide 44: Recovered Response Curves
Red
Green
RGB
Blue
High dynamic range imaging
Notes: 15

## Slide 45: The Radiance Map
High dynamic range imaging
Notes: 17

## Slide 46: Recovering HDR
1. Extract the radiance information from the photographs
2. Tone-map it into a single low dynamic range image
High dynamic range imaging
Notes: Basically, we have 2 steps to generate a better composition picture.
To turn a photograph into an HDR image, we first extract the radiance information from the photographs and then tone-map it into a single low dynamic range image.

## Slide 47
10-6
106
10-6
106
Real world
Picture
0 to 255
High dynamic range
High dynamic range imaging
Given radiance map
Goal: build a reasonable mapping function of radiance to pixel values

## Slide 48: Tone mapping Methods
Simple Gamma tone mapping
Gamma applied to each color channel independently
Input Image
Gamma applied to each channel
Gamma compression
High dynamic range imaging
Notes: Gamma compression)

## Slide 49: Tone mapping Methods
Intensity Gamma tone mapping
Splitting the image up into luminance and chrominance(L*a*b) components, and applying the mapping to the luminance channel
Input Image
Gamma applied to luminance
High dynamic range imaging
Notes: Obviously, this way works better!

## Slide 50: Chrominance and luminance
YUV color space
High dynamic range imaging
Notes: By the way, I think I have to show the basic conception of chrominance and luminance. Basically, it is another representation for color image. This is also called YUV color space. It is widely used on Television.
On the right side of our slide, we can see that this is a example of YUV color space. The top picture is represent in RGB value. The following pics are luminace part, and 2 chrominance part.

## Slide 51: Tone mapping Methods
Advanced mapping method
High dynamic range imaging
Notes: Unfortunately, when image has a really wide range of exposures, this global approach still fails to preserve details in regions with widely varying exposures.

## Slide 52: Tone mapping Methods
Advanced mapping method (using Edge-preserving filter)
High dynamic range imaging

## Slide 53: Outline
Photometric calibration
High dynamic range imaging
Image matting and compositing
Super-resolution and blur removal
Texture analysis and synthesis
Notes: In this Lecture, I will show you many interesting, recent techniques for capturing, modeling, and displaying of complex appearance phenomena.
I will cover topics of Photometric calibration, High dynamic range imaging, Super-resolution and blur removal, image matting and compositing, Texture analysis and synthesis.

## Slide 54: Image matting and compositing
Image matting and compositing
Notes: Actually, Image matting is commonly used in television and film production to composite a live actor in front of computer-generated image.
Or we can say, by using matting Power, super-man is able to fly everywhere. 

## Slide 55: Compositing Equation
B: background image
F: foreground image
C: composite image
Image matting and compositing
F
Notes: We first look at how compositing is done.
Basically, in the model, we use background, foreground, and alpha channel to describe this problem.
As show in the equation, this operator attenuates the influence of the background image B by a factor (1-alpha) and adds in the color values corresponding to the foreground element F.
During composting, given a foreground element including the foregound color F and an opacity image called alpha matte, and the background B, the composte C is computed by the composting equation shown here.

## Slide 56

F
B
C
foreground color
alpha matte
background plate
composite
compositing
equation
B
F
C
=0
Image matting and compositing
F
Notes: Here is the example.
We can see that, by using this technique, we can …..
Here, alpha matte acts like a switch to select foregound if it is white, background if it is black.
Most importantly, it is soft around the boundaries. The fractional alpha describe how much foreground and how much background should be taken. A soft alpha matte is very important for seamless composite.

## Slide 57: Compositing
Image matting and compositing
Alpha
1: means opaque,
0:means transparent
Fractional alpha is important!
With
binary
alpha
With
fractional
alpha
Notes: Most importantly, it is soft around the boundaries. The fractional alpha describe how much foreground and how much background should be taken. A soft alpha matte is very important for seamless composite.
We can see that, if we use binary alpha, the boundary is not smooth. Which makes the picture not that realistic.
Motion blur, small features (hair) cause partial
Occlusion
But How to get a reasonable alpha , usually we will use the technique of matting.!

## Slide 58: Matting
C
compositing
equation

F
B
Matting
Image matting and compositing
Notes: While, Matting is an inverse process to compositing. Given the observation C, essentially the composite, based on the compositing equation, we attempt to estimate the foreground color, the alpha matte and the background color. Which is far more challenging.
It is an under-costained problem, we have to solve 7 unknowns from 3 equations.

## Slide 59: Matting ambiguity
Known: C
Unknown: , F
7 unknowns: α and triplets for F and B
3 equations, one per color channel
F
Image matting and compositing
Notes: For matting problems, we only know Current picture.
we have to solve 7 unknowns from 3 equations

## Slide 60: Blue screen matting
C
F
B

F
Known: C,
Unknown: F
4 unknowns: α and triplets for F
3 equations, one per color channel
Image matting and compositing
Notes: Most times, we use a blue screen matting technique to reduce the number of unknowns.
Blue screen matting means filming an actor in front of a constant colored background.

## Slide 61: Traditional blue screen matting
Assume that blue b and green g channels of the foreground respect
For typically between 0.5 and 1.5
where are user parameters
Lots of refinements (see Smith & Blinn's paper)
Image matting and compositing

## Slide 62: Blue screen matting issues
Color limitation
– Annoying for blue-eyed people
adapt screen color (in particular green)
Shadows
– How to extract shadows cast on background
Image matting and compositing

## Slide 63: Natural image matting
Image matting and compositing
B
C
F

B
FG
BG
unknown

## Slide 64: Bayesian matting approach(Chuang 2001)
Given an input image with arbitrary background
The user specifies a coarse Trimap
(known Foreground, known background
and unknown region)
Goal: Estimate F, B, alpha in the unknown region
Image matting and compositing

## Slide 65: Bayesian matting approach(Chuang 2001)
Bayes theorem
Image matting and compositing
Notes: First let’s get a review of bayes theorem.

## Slide 66: Bayesian matting approach(Chuang 2001)
Image matting and compositing
Notes: Given F, B and Alpha, probability that we observe C

## Slide 67: Bayesian matting approach(Chuang 2001)
We must try to build a probability distribution for the unknown regions.
Image matting and compositing

## Slide 68: Bayesian matting approach(Chuang 2001)
Log likelihood
Image matting and compositing
Notes: This model suppose that the noise is respect to gaussian noise model.

## Slide 69: Bayesian matting approach(Chuang 2001)
Prior probabilities
SAME for B
Image matting and compositing
Notes: Fror the prior probabilities, we suppose within each pixel’s neighborhood N, it is a elliptical Gaussian distribution.

## Slide 70: Bayesian matting approach(Chuang 2001)
Prior probabilities
In this work, we assume that log likelihood for the opacity is constant.
Ignort it.
Image matting and compositing

## Slide 71: Bayesian matting approach(Chuang 2001)
Image matting and compositing

## Slide 72: Bayesian matting approach(Chuang 2001)
Solve math problem: (for constant)
Image matting and compositing

## Slide 73: Bayesian matting approach(Chuang 2001)
Solve math problem: for constant
Image matting and compositing

## Slide 74: Bayesian matting approach(Chuang 2001)
Solve math problem:
1. The user specifies a trimap
2. Compute Gaussian distributions for foreground and background regions
3. Iterate
  – Keep α constant, solve for F & B (for each pixel)
  – Keep F & B constant, solve for α (for each pixel)
Note that pixels are treated independently
Image matting and compositing

## Slide 75: Bayesian matting approach(Chuang 2001)
Results:
Image matting and compositing

## Slide 76: Outline
Photometric calibration
High dynamic range imaging
Image matting and compositing
Super-resolution and blur removal
Texture analysis and synthesis
Notes: In this Lecture, I will show you many interesting, recent techniques for capturing, modeling, and displaying of complex appearance phenomena.
I will cover topics of Photometric calibration, High dynamic range imaging, Super-resolution and blur removal, image matting and compositing, Texture analysis and synthesis.

## Slide 77: How to increase resolution
Possible ways for increasing an image resolution:
  – Reducing pixel size.
  – Increase the chip-size.
  – Super-resolution.
Image matting and compositing

## Slide 78: How to increase resolution
Reduce pixel size:
  Increase the number of pixels per unit area.
Advantage:
  Increases spatial resolution.
Disadvantage:
  Noise introduced.
  As the pixel size decreases, the amount of light decreases.
Image matting and compositing

## Slide 79: How to increase resolution
Increase the chip size (HW):
Advantage:
  Enhances spatial resolution.
Disadvantage:
  High cost for high precision optics.
Image matting and compositing

## Slide 80: How to increase resolution
Superresolution (SR):
  Process of combining multiple low resolution images to form a high resolution image.
Advantages:
  Cost less than comparable approaches.
  LR imaging systems can still be utilized.
Image matting and compositing

## Slide 81: Super-resolution
Obtaining a HR image from one or multiple LR images .
Super-resolution and blur removal

## Slide 82: Super-resolution

## Slide 83: Outline
Photometric calibration
High dynamic range imaging
Image matting and compositing
Super-resolution and blur removal
Texture analysis and synthesis
Notes: In this Lecture, I will show you many interesting, recent techniques for capturing, modeling, and displaying of complex appearance phenomena.
I will cover topics of Photometric calibration, High dynamic range imaging, Super-resolution and blur removal, image matting and compositing, Texture analysis and synthesis.

## Slide 84
Texture analysis and synthesis

## Slide 85: Reference
[1]Richard Szeliski,Computer Vision:Algorithms and Applications
[2]Chuang, Y. Y., Curless, B., Salesin, D. H., & Szeliski, R. (2001). A bayesian approach to digital matting. In Computer Vision and Pattern Recognition, 2001. CVPR 2001. Proceedings of the 2001 IEEE Computer Society Conference on(Vol. 2, pp. II-264). IEEE.
[3] Liu, C., Freeman, W. T., Szeliski, R., & Kang, S. B. (2006, June). Noise estimation from a single image. In Computer Vision and Pattern Recognition, 2006 IEEE Computer Society Conference on (Vol. 1, pp. 901-908). IEEE.
[4] Kim, S. J., & Pollefeys, M. (2008). Robust radiometric calibration and vignetting correction. Pattern Analysis and Machine Intelligence, IEEE Transactions on, 30(4), 562-576.
[5] Debevec, P. E., & Malik, J. (2008, August). Recovering high dynamic range radiance maps from photographs. In ACM SIGGRAPH 2008 classes (p. 31). ACM.
Texture analysis and synthesis

## Slide 86: Thanks!
Seminar on computational photography
Course advisor: Dr. Shirani
Web: http://sdfsfalkfjasdlfj
Email: dengx23@mcmaster.ca
Xiaowei Deng @Mac, Dec. 2013